## Slide 1: Paper Microfluidic Detection of Heavy Metal Using Biopolymers
Wimonmas Areekul
Laboratory of Biological, Biomimetic, Eco-friendly Materials
Division of Environmental Science and Engineering
Notes: Visual image

## Slide 2
Introduction: SALSA
Lucas-Washburn Equation
Where L = Flow distance
t = Time
R = Capillary radius
γ = Surface tension
θ = Water contact angle
η = Dynamic viscosity
System Automated Loading for Sample Analysis
2/23

## Slide 3: Introduction: Literature review
Paper microfluidic detection
of PFAS* using biopolymers
*Per- and polyfluoroalkyl substances
Three PFAS types – PFOA, PFOS, GenX
Three machine learning models – XGBoost, Random Forest, SVMs (Support Vector Machine)
Reagents – Bovine serum albumin (BSA), Lysozome, Myoglobin, L-lysine, Glycine, Glutamine, L-aspartic acid
Accuracies for PFAS type classification
However, PFAS pollution is still not
a significant problem in Thailand
Model | Accuracy (%)
XGBoost | 91.7
Random Forest | 94.7
SVM | 93.7
3/23

## Slide 4: Introduction: Motivation
Emerging Heavy Metal Contamination in Northern Thailand
Arsenic detected
in Kok river
Arsenic + Chromium detected
in Salawin river
Apr 2025
Nov 2025
Present
(Pollution Control Department, 2025)
Infected, mutant fish
(Source: ThaiPBS)
Bad water quality
(Source: Mongabay)
4/23

## Slide 5: Introduction: Motivation
Problems of conventional methods for heavy metal detection
“The use of biopolymers provides sustainable solutions”
High
cost
Centralized
laboratory
Intensive
resources
Reverse
contamination
5/23

## Slide 6: Experiment I
Classification of arsenic (As), chromium (Cr) and cadmium (Cd) using chitosan and poly-L-lysine

## Slide 7
Methodology
Factor | Levels
Heavy metal | As, Cr, Cd
Heavy metal concentration (ppb) | 0, 1, 10, 100 (As) 0, 5, 50, 500 (Cr, Cd)
Reagent | Chitosan, Poly-L-lysine
Reagent concentration (ppb) | 0, 1, 100, 10000
Conditions | Chitosan: 300 µM CH3COOH Poly-L-lysine: DI
Surface water quality standard for heavy metals
Dilution
preparation
Vortex
Mixing
Paper chip loading
and SALSA operation
Flow profile analysis + Machine learning
Heavy metal | Concentration (ppb)
Arsenic (As) | 10
Chromium (Cr) | 50
Cadmium (Cd) | 50
7/23

## Slide 8
Results: Overall accuracy
Model | Reagent | Mean Score | Std Dev
XGBoost | all | 0.7665 | 0.0938
 | Chi | 0.6251 | 0.0891
 | Lys | 0.7624 | 0.1057
Random Forest | all | 0.9333 | 0.0757
 | Chi | 0.6917 | 0.0864
 | Lys | 0.8750 | 0.1179
SVM | all | 0.9583 | 0.0417
 | Chi | 0.8750 | 0.0780
 | Lys | 0.8750 | 0.0977
XGBoost
Random Forest
SVM
8/23
The results from Random Forest and SVM models show high accuracy (> 90%), however, the result from XGBoost model still shows the accuracy less than 80%

## Slide 9
Results: Chitosan accuracy
Model | Reagent | Mean Score | Std Dev
XGBoost | all | 0.7665 | 0.0938
 | Chi | 0.6251 | 0.0891
 | Lys | 0.7624 | 0.1057
Random Forest | all | 0.9333 | 0.0757
 | Chi | 0.6917 | 0.0864
 | Lys | 0.8750 | 0.1179
SVM | all | 0.9583 | 0.0417
 | Chi | 0.8750 | 0.0780
 | Lys | 0.8750 | 0.0977
XGBoost
Random Forest
SVM
9/23
Although the result from SVM model shows high accuracy (> 80%), the results from XGBoost and Random Forest models show low accuracy (< 70%)
Future work - Conduct the experiment using other biopolymers

## Slide 10
Results: Poly-L-lysine accuracy
10/23
Model | Reagent | Mean Score | Std Dev
XGBoost | all | 0.7665 | 0.0938
 | Chi | 0.6251 | 0.0891
 | Lys | 0.7624 | 0.1057
Random Forest | all | 0.9333 | 0.0757
 | Chi | 0.6917 | 0.0864
 | Lys | 0.8750 | 0.1179
SVM | all | 0.9583 | 0.0417
 | Chi | 0.8750 | 0.0780
 | Lys | 0.8750 | 0.0977
XGBoost
Random Forest
SVM
The results from Random Forest and SVM models show high accuracy (> 80%), however, the result from XGBoost still shows the accuracy less than 80%
Future work - Conduct the experiment in other conditions than DI water and blend poly-L-lysine with other biopolymers to improve the accuracy

## Slide 11: Experiment II
Classification of arsenic (As), cadmium (Cd) and cobalt (Co) using alginate, tannin and gallic acid

## Slide 12
Methodology
Factor | Levels
Heavy metal | As, Cd, Co
Heavy metal concentration (ppb) | 0, 1, 10, 100 (As, Co) 0, 5, 50, 500 (Cd)
Reagent | Alginate, Tannin, Gallic acid
Reagent concentration (ppb) | 0, 1, 100, 10000
Conditions | DI, 0.1 M PBS, 0.7 M NaCl, RSW
Surface water quality standard for heavy metals
Dilution
preparation
Vortex
Mixing
Paper chip loading
and SALSA operation
Flow profile analysis + Machine learning
7/13
Heavy metal | Concentration (ppb)
Arsenic (As) | 10
Cadmium (Cd) | 50
Cobalt (Co) | -
12/23

## Slide 13
Results: Overall accuracy
Model | Mean Score | Std Dev
XGBoost | 0.9937 | 0.017
Random Forest | 1.0000 | 0.000
SVM | 1.0000 | 0.000
XGBoost
Random Forest
SVM
13/23
Primary accuracy: XGBoost 99.37% (25-fold repeated CV, 1.7%) – statistically robust estimate
Confirmed by Random Forest (RF) and SVM: 100% under chip-aware GroupKFold (k=5) evaluation
Consistent across 3 independent model -> result reflects the data, not the model
Shuffled-label control: 32.3% -> signal is genuine, not artefact

## Slide 14
Results: Accuracy by reagent
Model | Reagent | Mean Score | Std Dev
XGBoost | all | 0.9937 | 0.017
 | Alg | 0.9335 | 0.056
 | Tan | 0.9376 | 0.054
 | Gal | 0.9520 | 0.054
Random Forest | all | 1.0000 | 0.000
 | Alg | 1.0000 | 0.000
 | Tan | 0.9917 | 0.019
 | Gal | 1.0000 | 0.000
SVM | all | 1.0000 | 0.000
 | Alg | 1.0000 | 0.000
 | Tan | 0.9917 | 0.019
 | Gal | 1.0000 | 0.000
14/23
High accuracy confirmed across all models
Largest XGBoost variance among reagents -> signal slightly condition-sensitive
XGBoost
Random Forest
SVM

## Slide 15
Results: Accuracy by reagent
Model | Reagent | Mean Score | Std Dev
XGBoost | all | 0.9937 | 0.017
 | Alg | 0.9335 | 0.056
 | Tan | 0.9376 | 0.054
 | Gal | 0.9520 | 0.054
Random Forest | all | 1.0000 | 0.000
 | Alg | 1.0000 | 0.000
 | Tan | 0.9917 | 0.019
 | Gal | 1.0000 | 0.000
SVM | all | 1.0000 | 0.000
 | Alg | 1.0000 | 0.000
 | Tan | 0.9917 | 0.019
 | Gal | 1.0000 | 0.000
15/23
XGBoost
Random Forest
SVM
Lowest accuracy of three reagents across all models
Tannin’s polyphenolic structure may produce overlapping electrochemical signal signatures between certain metal species under some buffer conditions, making the classification boundary less sharp compared to other two reagents

## Slide 16
Results: Accuracy by reagent
Model | Reagent | Mean Score | Std Dev
XGBoost | all | 0.9937 | 0.017
 | Alg | 0.9335 | 0.056
 | Tan | 0.9376 | 0.054
 | Gal | 0.9520 | 0.054
Random Forest | all | 1.0000 | 0.000
 | Alg | 1.0000 | 0.000
 | Tan | 0.9917 | 0.019
 | Gal | 1.0000 | 0.000
SVM | all | 1.0000 | 0.000
 | Alg | 1.0000 | 0.000
 | Tan | 0.9917 | 0.019
 | Gal | 1.0000 | 0.000
16/23
XGBoost
Random Forest
SVM
Best-performing reagent across all models

## Slide 17
Results: Accuracy by condition
Model | Condition | Mean Score | Std Dev
XGBoost | all | 0.9937 | 0.017
 | DI | 0.8958 | 0.080
 | PBS | 0.9088 | 0.067
 | NaCl | 0.9645 | 0.029
 | RSW | 0.9540 | 0.053
Random Forest | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 0.9583 | 0.042
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
SVM | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 1.0000 | 0.000
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
17/23
XGBoost shows lowest accuracy and highest variance of all conditions
RF and SVM each misclassified one sample
XGBoost
Random Forest
SVM

## Slide 18
Results: Accuracy by condition
Model | Condition | Mean Score | Std Dev
XGBoost | all | 0.9937 | 0.017
 | DI | 0.8958 | 0.080
 | PBS | 0.9088 | 0.067
 | NaCl | 0.9645 | 0.029
 | RSW | 0.9540 | 0.053
Random Forest | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 0.9583 | 0.042
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
SVM | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 1.0000 | 0.000
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
18/23
XGBoost
Random Forest
SVM
Only condition where RF drops below 99%
Phosphate and saline components may interact with metal species or reagents, causing signal overlap -> priority target for measurement optimization

## Slide 19
Results: Accuracy by condition
Model | Condition | Mean Score | Std Dev
XGBoost | all | 0.9937 | 0.017
 | DI | 0.8958 | 0.080
 | PBS | 0.9088 | 0.067
 | NaCl | 0.9645 | 0.029
 | RSW | 0.9540 | 0.053
Random Forest | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 0.9583 | 0.042
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
SVM | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 1.0000 | 0.000
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
19/23
XGBoost
Random Forest
SVM
Best-performing condition across all models

## Slide 20
Results: Accuracy by condition
Model | Condition | Mean Score | Std Dev
XGBoost | all | 0.9937 | 0.017
 | DI | 0.8958 | 0.080
 | PBS | 0.9088 | 0.067
 | NaCl | 0.9645 | 0.029
 | RSW | 0.9540 | 0.053
Random Forest | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 0.9583 | 0.042
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
SVM | all | 1.0000 | 0.000
 | DI | 0.9917 | 0.019
 | PBS | 1.0000 | 0.000
 | NaCl | 1.0000 | 0.000
 | RSW | 1.0000 | 0.000
20/23
XGBoost
Random Forest
SVM
Achieved strong classification performance
Demonstrates applicability to real environmental water sample conditions

## Slide 21
Overfitting analysis
7/13
21/23
Shuffled-label control (32.3%) is near 3-class chance (33.3%) -> confirms real signal
1-NN leave-one-out (95.8%) is close to XGBoost (99.4%), RF (100%) and SVM (100%) -> confirms that raw feature space is separable without any model fitting
Shuffled labels (permutation control)
1-nearest neighbour classifier
with leave-one-out evaluation

## Slide 22
Overfitting analysis
7/13
22/23
Best single feature accuracy (67.7%) is far below XGBoost (99.4%), RF (100%) and SVM (100%) -> none of the three independent models is reducible to one trivially separating column; each genuinely integrates information
Mean between-class separation of 1.60 confirms that arsenic (AS), cadmium (CD) and cobalt (CO) occupy genuinely distinct regions of feature space -> genuine physicochemical contrast between metals
Best single feature accuracy
Between-class feature separation

## Slide 23
Next step: thesis
Factor | Levels
Heavy metal | As, Cr(3+ and 6+), Cd, Co
Heavy metal concentration (ppb) | 0, 1, 10, 100 (As, Co) 0, 5, 50, 500 (Cr, Cd)
Reagent | Chitosan, Alginate, Tannin
Reagent concentration (ppb) | 0, 1, 100, 10000
Conditions | DI, 0.1 M PBS, Chaopraya river sample, Hyeongsan river sample
7/13
23/23
 | As | Cr3+ | Cr6+ | Cd | Co
Chitosan (4 conditions) | 960 combinations 8 measurement per combination 7,680 measurements in total |  |  |  | 
Alginate (4 conditions) |  |  |  |  | 
Tannin (4 conditions) |  |  |  |  | 
Current available salsa data from previous experiment => 224 combinations (23.33%)
Complete all salsa data collection within December

## Slide 24
Thank you